## Slide 1: Simplification of Boolean Expression & Logic circuit drawing
Alokedip Choudhuri(510514064)
Pooja Dashottar(510514057)
Under the guidance of Prof. Apurba Sarkar
Department of Computer Science and Technology
IIEST,Shibpur

## Slide 2: Why we need to simplify the Boolean expression?
To minimize the cost to design the circuit.
To reduce the complexity of the circuit.

## Slide 3: Different methods for simplifying a Boolean expression
There are various methods for simplifying a Boolean expression. Amongst them two methods are very famous , they are:
1. Karnaugh Map
2. Quine-McCluskey method(Well known Tabular Method)

## Slide 4: Limitation of Karnaugh Map…

## Slide 5: Algorithm for simplifying a Boolean expression and circuit drawing
Suppose we are given a Boolean function F , such that
F(w ,x ,y ,z )=∑(1,4,6,7,8,9,10,11,15)
These are the min terms of the Boolean expression ‘F’

## Slide 6: Quine-Mccluskey method(Tabular-Method)
Step1:
Group the min terms according to the no of 1’s into them.
So the grouping will look like for that particular example:
0001 1
0100 4
1000 8
0110 6
1001 9
1010 10
0111 7
1011 11
1111 15
Group-3
Group-2
Group-1
Group-4

## Slide 7: Next step:
Step2:
      After step 2 the column will look like:
      1 , 9 (8 ->4th bit difference)
      4 , 6 (2->2nd bit difference)
      8 , 9 (1->1st bit difference)
      8 , 10 (2->2nd bit difference)
      6 , 7 (1->1st bit difference)
      9 , 11 (2->2nd bit difference)
      10 , 11 (1->1st bit difference)
      7 , 15 (8->4th bit difference)
      11 , 15 (4->3rd bit difference)

## Slide 8: Next step:
Step3:
Repeat step 2 until we will get pairs of min terms which has difference in more than one bit or there is no difference at all.
So according to this recursive step at the end we will get the 3rd column :

## Slide 9: Steps:
0001 1 * 1 , 9 8 , 9 , 10 , 11
0100 4 * 4 , 6 8 , 10 , 9 , 11
1000 8 * 8 , 9 *
8 , 10 *
0110 6 *
1001 9 * 6 , 7
1010 10 * 9 , 11 *
10 , 11 *
0111 7 *
1011 11 * 7 , 15
11 , 15
1111 15 *
In this column all the pairs have no difference in any bit so the recursive call will terminate after this column completion.

## Slide 10: Selection of prime implicants:
Step4:
  After step 3 all unchecked term and the combined terms in last columns form the prime implicants.
  But among them those prime implicants that will simplify the Boolean expression are called “Essential Prime Implicants”.
  For this case to find the essential prime implicants we will follow the following method:

## Slide 11: Table to determine the essential prime implicants
1 4 6 7 8 9 10 11 15
x’y’z 1 , 9 x x
w’xz’ 4 , 6 x x
w’xy 6 , 15 x x
xyz 7 , 15 x x
wyz 11 , 15 x x
wx’ 8 , 9 , 10 , 11 x x x x
E E E E E E E So the simplified function F(w , x , y , z)=x’y’z + w’xz’ + xyz + wx’

## Slide 12: Next step after getting simplified Boolean expression:
convert to postfix:
After getting the simplified form we have to convert the Boolean expression into postfix form choosing stack as a data-structure.
So for the current example the postfix form will be:
Infix: x’y’z + w’xz’ + xyz + wx’
Postfix: x’y’*z*w’x*z’*+wx’*xy*z*++

## Slide 13: Postfix evaluation and circuit drawing:
Postfix evaluation:
To draw the circuit we have to evaluate the postfix while evaluating the postfix we have chosen stack as a data structure and to draw the circuit while pushing the resultant value of two operands we just draw the corresponding logic circuit. In this way we have drawn the logic circuit for the given example:
Like if we have popped two successive operand and the corresponding operator is ‘*’ then we just connect the two line segments with an AND gate naming the segments with the operand variable name.
same as if we have popped two successive operand and the corresponding operator is ‘+’ then we just connect the two line segments with an OR gate naming the segments with the operand variable name.

## Slide 14: Step by step logic circuit for the example:
Working final expression: x’y’*z*w’x*z’*+wx’*xy*z*++
x’
y’ Assumption: assume that the negation of the variables are available directly.
x’y’*

## Slide 15: Step by step logic circuit for the example:
Working final expression: x’y’*z*w’x*z’*+wx’*xy*z*++
x’
y’
z
x’y’*
x’y’*z*

## Slide 16: Step by step logic circuit for the example:
Working final expression: x’y’*z*w’x*z’*+wx’*xy*z*++
x’
y’
z
w’
x
x’y’*
x’y’*z*
w’x*

## Slide 17: Step by step logic circuit for the example:
Working final expression: x’y’*z*w’x*z’*+wx’*xy*z*++
x’
y’
z
w’
x
z’
x’y’*
x’y’*z*
w’x*
w’x*z’*

## Slide 18: Step by step logic circuit for the example:
Working final expression: x’y’*z*w’x*z’*+wx’*xy*z*++
x’
y’
z
w’
x
z’
x’y’*
x’y’*z*
w’x*
w’x*z’*
x’y’*z*w’x*z’*+

## Slide 19: Step by step logic circuit for the example:
Working final expression: x’y’*z*w’x*z’*+wx’*xy*z*++
x’
y’
z
w’
x
z’
w
x’
x’y’*
x’y’*z*
w’x*
w’x*z’*
x’y’*z*w’x*z’*+
wx*

## Slide 20: Step by step logic circuit for the example:
Working final expression: x’y’*z*w’x*z’*+wx’*xy*z*++
x’
y’
z
w’
x
z’ x
w y
x ’ z
x’y’*
x’y’*z*
w’x*
w’x*z’*
x’y’*z*w’x*z’*+
wx*
xy*z*

## Slide 21: Step by step logic circuit for the example:
Working final expression: x’y’*z*w’x*z’*+wx’*xy*z*++
x’
y’
z
w’
x
z’ x
w y
x ’ z
x’y’*
x’y’*z*
w’x*
w’x*z’*
x’y’*z*w’x*z’*+
wx*
xy*z*
wx’*xy*z*+

## Slide 22: Step by step logic circuit for the example:
Working final expression: x’y’*z*w’x*z’*+wx’*xy*z*++
x’
y’
z
w’
x
z’ x
w y
x ’ z
x’y’*
x’y’*z*
w’x*
w’x*z’*
x’y’*z*w’x*z’*+
wx*
xy*z*
wx’*xy*z*+
result

## Slide 23: Complexity analysis:
Although more practical than “Karnaugh Mapping” when dealing with more than four variables, the “Quine–McCluskey” algorithm also has a limited range of use since the problem it solves is NP-hard:
The runtime of the “Quine–McCluskey” algorithm grows exponentially with the number of variables. It can be shown that for a function of n variables the upper bound on the number of prime implicants is O(3n/n).
Example:
If n = 32 there may be over 6.5 * 1015 prime implicants.

## Slide 24: Thank you